JOB-SITE REQUIREMENTS

- Final grading should be complete. Surface drainage should direct water away from the building.

- Crawl space must be dry and well ventilated.

- The building must be closed in with all outside windows and doors in place.

- All concrete, masonry, sheetrock and framing members, etc., should be thoroughly dry before flooring is delivered to the job-site.

- IMPORTANT - In warm months, the building must be well ventilated; in winter, a temperature of 65-70 degrees should be maintained at least five days before the flooring is delivered.

- Subfloors shall be broom swept and free from squeaks, unevenness or surface imperfections, i.e. holes in subfloors, nails, low/high spots.

- 220 volt, 30 amp power must be within 100 feet of the work area via standard electrical outlets.

- There should be 1/2” expansion at all walls. If the baseboards are a ½” thick or narrower, installation of baseshoe or holding sheetrock up is recommended.

10.) The flooring should be stocked at the job-site five (10) days prior to installation.

**